## Slide 1: A Nationwide Study of REEs in Geothermal and Produced Waters: Final Results DOE Project Number: EE0007603
Charles Nye (UW), Ghanashyam Neupane (INL), Scott Quillinan (UW)
February 11, 2019
Image from Scott Quillinan

## Slide 2: Project Motivation
While these elements have a growing strategic importance in our daily lives an economic domestic resource does not exist.
In addition to the lack of domestic resources, we recognize that another domestic challenge is the management and disposal of brines co-produced alongside oil and gas.
Images from Wikipedia [1] [2] [3]
Rare earth elements (REEs) play a critical role in the move towards 100% renewable energy portfolios.

## Slide 3: Project Goals
Images from Hari Neupane
and Tom Moore
Contribute to a national database of rare earth element and high value materials in oil and gas produced waters and other geothermal waters
Refine methodologies for REE analysis in highly saline fluids
Develop a statistical screening tool for geologic prospecting
Techno-economic assessment
224=Nwater
83=Nrock

## Slide 4: Ad Hoc Results
Images from Davin Bagdonas, Mark Engle, and Charles Nye
Carbonate Rocks contain little or no REEs
Serendipitous support for Nealson et al., (2009)
Continental REEs are unlike existing rock (NASC) and ocean (NPDW) normalizations

## Slide 5
Images from Charles Nye

## Slide 6
Images from Charles Nye
“A Machine Learning Approach to Predicting Rare Earth Element Potential in Produced and Geothermal Waters of the United States”
Mark A. Engle, Charles W. Nye, Ghanashyam Neupane, Scott A. Quillinan, J. Fred McLaughlin, Travis McLing, Josep A. Martín-Fernández
Natural Resources Research (In review) expected Q2 2019.

## Slide 7: Results: 1/5
Image from Charles Nye
Sources: Nozaki 2001, Davies 1964, Matthai et al. 1957, Lieberman 2000
REEs sometimes occur in continental groundwater in excess of 1000-times their seawater concentrations.
Imperative to surpass Seawater
Europium: Blessing? Curse?
Site-Specific assessments to match market.

## Slide 8: Results: 2/5
Image from Mark Engle
REEs occur in at least ng/L concentration in all continental groundwaters.
Some are barely over 1mg/L (ppt)
All are measurable with INL’s method
Extreme economics would allow anyone to supply REEs.

## Slide 9: Results: 3/5
Image from Mark Engle
Many principles for REE in rock should work for water.
Deviation from simple filling order: [Xe]6s24f75d1
Total pairing ≈ orbital energy difference makes larger radius.
Natural Aqueous Behavior Suggests Distinctive Behavior between Light and Heavy REEs, matching Atomic Numbers 57-64 and 65-71.

## Slide 10: Results: 4/5
Image from Mark Engle
Rock type does not match, but individual rocks may match individual waters - challenging to construct in ESOM.
Location specific processes may explain REE enrichment.
Lithology, temperature, and salinity do not have a significant relationship to REE concentration.

## Slide 11: Results: 5/5
Images from Charles Nye and Ron Blakey
The four HREE enriched samples have a significant shale fraction. Cannonball sea was persistent in this area.
REE concentrations are often spatially co-associated.

## Slide 12: Future Work: 1/3
Image from Charles Nye
Hunt for the unknown variable that controls REE concentration.
Basin-by-basin behavior is not random.
Minor components of Lithology? Organic fraction? Clastics?
Depositional History? Coastal sands == deep ocean shale?
Flushing events limited by re-equilibration?

## Slide 13: Future Work: 2/3
Image from Charles Nye
Collect a bigger sample set, maybe with new water types.
Oklahoma, N. Louisiana, S. Illinois, and Utah-Colorado border
Anomaly detection
Breakthrough on the unknown variable
“Used” water: cooling, solvay, purification, concentrate, coal power ash ponds?

## Slide 14: Future Work: 3/3
Images from Charles Nye and Hari Neupane
Comparison and validation of new analytical techniques.
Low-volume TIMS (Thermal ionization mass spectrometry)?
Naive analysis on an Agilent 8900 Triple Quadrapole?

## Slide 15: Everything is on the GDR
Final report in review
Small number of non-material edits

## Slide 16: Acknowledgements
Team Members:
Funding sources:
DOE: EERE
Carbon Management
Institute

## Slide 17: Further Resources
Fernandez V. 2017 Rare-earth elements market: a historical and financial perspective Res. Policy, 53 (2017), pp. 26-45, 10.1016/j.resourpol.2017.05.010
Nozaki 2001 Rare Earth Elements and their Isotopes in the Ocean
doi:10.1006/rwos.2001.0284
Blakey, Ron C., 2104, Paleogeography and Paleotectonics of the Western Interior Seaway, AAPG Search and Discovery Article #30392
Quillinan S., Nye C., Engle M., Bartos T., Neupane G., Brant J., Bagdonas D., McLing T., McLaughlin J. F. (2019). Assessing rare earth element concentrations in geothermal and oil and gas produced waters: A potential domestic source of strategic mineral commodities. Final Report to U.S. Department of Energy, Geothermal Technologies Office, 184 pages. Award Number: DE-EE0007603, (In review)

## Slide 18: Support Slides

## Slide 19
Industrial power station ash ponds and coal seams look promising!
These are very clean waters. That opens up clever processing options.
Coal seam pool
Ash pond
Ash pond