## Slide 1: Programming the ATtiny Microcontroller
The ATtiny microcontroller is programmed using C code
Programs are very similar to those on a standard Arduino
Key differences include
  Only a few pins are available, so it is less capable than the Arduino UNO
  For ATtiny 25 and 45 there is less memory available than ATtiny 85, so program space is limited.
  There is no USB port so how do we upload the program?

## Slide 2: Ways to upload a program to ATtiny
One can buy an inexpensive programmer
  Here’s one from Sparkfun for $15.95 (there are cheaper ones out there)
Or, build a simple circuit based on a standard Arduino UNO.
  This is our approach. It allows us to program 100 ATtiny’s by having 5-6 students working simultaneously, each using their own Arduino setup.
  This is the subject of this presentation
Plug ATtiny in here

## Slide 3: This is the ATtiny Programmer circuit
The three LEDs don’t do much
Red (pin 8) = error
Green (pin 7) = communication in progress
Blue (pin 9) = heartbeat
Be Sure to place the ATtiny as shown.
The “Dot” should be on the left side!
(This works for ATtiny25, ATtiny45, or ATtiny85)
220
Dot

## Slide 4: Arduino as an “In-System Programmer” (ISP)
Prepare your Arduino to be an ATtiny programmer
  To do this, use the program “ArduinoISP”, which is provided in Arduino Examples
  Open it like this:
File -> Examples -> 11.ArduinoISP -> ArduinoISP
Upload it to your Arduino.
  You should see the “heartbeat” on the blue LED. It’s ALIVE!
  Your Arduino is now (almost) ready to program the ATtiny
Note that we haven’t yet discussed the program that we want to install into the ATtiny’s memory.
  That will come later - First we have more work to do!

## Slide 5: Preparing Arduino to be an ATtiny programmer
The Arduino IDE needs to know details about the chip it will be programming. In this case it needs more info about the ATtiny.
The following six slides add ATtiny board information to Arduino IDE
Slides outlined in RED were taken from the tutorial at: http://highlowtech.org/?p=1695

## Slide 6
Copy and paste the following URL into the field :
https://raw.githubusercontent.com/damellis/attiny/ide-1.6.x-boards-manager/package_damellis_attiny_index.json
Click the OK button to save your updated preferences
(1)
Paste URL Here

## Slide 7
Click
Here
(2)

## Slide 8
(3)
Click “More Info”

## Slide 9
(4)

## Slide 10
(5)

## Slide 11
(6)

## Slide 12: Finally – upload a program into ATtiny memory
Suppose the program we want to store into the ATtiny is called: ATprogram.ino. Open this file in a new Arduino window.
In the Tools menu make sure the following items are set:
  Board: ATtiny25/45/85
  Processor: ATtiny85 (or ATtiny45 or ATtiny25 depending on your ATTINY)
  Clock: Internal 1 MHz (default)
  Programmer: change from: “AVRISP mkII” (which is for normal Arduino use) to: “Arduino as ISP”
  Don’t forget to set Tools->Port to the correct COM number before proceeding
See screengrab next page

## Slide 13: Arduino IDE Tools Setup
Your “Tools” menu should look like this!

## Slide 14: Your Arduino is now an ATtiny Programmer! Just click “Upload” and hope for best.
Things are different than our usual Arduino upload
  In the past, “Upload” transfers the current program into Arduino’s memory
  But now, the program is not uploaded to Arduino memory, instead it is transferred into ATtiny memory
Upload

## Slide 15: TESTING
Assuming your program runs the Blink program on ATtiny pin 6, you can test for success as follows.
Move the ATtiny to a blank part of the breadboard
Connect jumpers and LED as shown.
On Power-up, ATtiny should run the Blink program
You’re done!
  Remove the ATtiny and install it in its own circuit board
Notes: This test only works for the program (ATprogram.ino ) supplied for this workshop.
It was written so that it always runs the Blink program on bootup.
Other programs may not do this, so