## Slide 1: ATtiny Workshop. Background Material
Electrical and Computer Engineering Department
University of Wyoming

## Slide 2: Background Information
Miscellaneous Information about ATtiny microcontroller
Schematics and C code
Cost of parts
Workshop details

## Slide 3: What is an ATtiny?
Smaller version of microcontroller used in Arduino Uno
  Except uses 3.3 Volts and there is no USB connection
Many versions. Most popular are:
  ATtiny45 has 4096 bytes of program memory
  ATtiny85 has 8192 bytes of program memory
  Both work for this workshop – get whichever is cheaper
  (ATtiny25 doesn’t have enough memory)
Programmed in C using the standard Arduino system, just like the Uno.
  Uploading programs to the ATtiny is different. Please see companion documentation for details.
  Programs are available by contacting esp4t_tech@uwyo or the author at kubichek@uwyo.edu

## Slide 4: ATtiny Pins
Pin 1: It is not recommended to use this pin as it is needed during the upload process.
Pins 2 and 3: Digital GPIO 3 and 4, and Analog A3 and A4
Pins 5 and 6: Digital GPIO 0 and 1
Pin 7: GPIO 2 and analog A1
Physical pin numbers are not used in the Arduino programs.
The following designations are used instead:

## Slide 5: Project 1: Light Sensor Information
Pushbuttons are connected to pins 2 and 3.
Output LEDs are on pins 5 and 6.
  Parts count minimized by not using current limiting resistors on LEDs
  Not needed since 3V coin cell has sufficient internal resistance.
Photoresistor is in series with resistor to form a “voltage divider”.
Notes: A voltage divider network is just two resistors in series. The voltage measured at their junction is directly related to resistance of the photoresistor, which depends on light level.
Using a voltage divider is necessary since the ATtiny can only measure voltage, not resistance

## Slide 6: Project 2: Game Mode Information
For game mode we need one more LED.
The photoresistor is removed and an LED is added
The resistor is retained as it does no harm, and keeping it is easier than removing it
Added LED

## Slide 7: How does program know whether breadboard is set up for light sensor mode or game mode?
Voltage on pin 7 (pinno) is different depending on whether there is an LED or photoresistor connected.
Empirically the voltage was measured for each case; a function “checkpin” was written to determine which case applies

## Slide 8: Materials
Materials ordered for batch of 100 kits (12/17). About $3 per kit.
Item | Package | Price | Quantity | Link
Photoresistor | 50 | $6.99 | 2 | https://www.amazon.com/Inductor-Sensor-Sensitive-Resistor-Photoresistor/dp/B01FDGUM8K/ref=sr_1_3?s=industrial&ie=UTF8&qid=1510693400&sr=1-3&keywords=light+sensitive+resistors+pcs&dpID=51pJND-tnfL&preST=_SX342_QL70_&dpSrc=srch
LED (5 mm) | 450 | $14.99 | 1 | https://www.amazon.com/dp/B073QMYKDM/ref=sxbs_sxwds-stvp_3?pf_rd_m=ATVPDKIKX0DER&pf_rd_p=3341940462&pd_rd_wg=Vysbb&pf_rd_r=SZPF9VGSZV8V6CEGDCRW&pf_rd_s=desktop-sx-bottom-slot&pf_rd_t=301&pd_rd_i=B073QMYKDM&pd_rd_w=4pid5&pf_rd_i=5mm+LED+pcs+arduino&pd_rd_r=ec8e231c-de43-4498-a463-1e41085b58c5&ie=UTF8&qid=1510693816&sr=3
Resistors: 220 | 250 | $8.01 | 1 | https://www.amazon.com/dp/B01LWXKN3X/ref=biss_dp_t_asn
Resistors: 1K | 250 | $8.01 | 1 | https://www.amazon.com/dp/B01LX9A31P/ref=biss_dp_t_asn
Resistors: 10K | 250 | $8.01 | 1 | https://www.amazon.com/dp/B01LY8BRJF/ref=biss_dp_t_asn
Pushbuttons | 100 | $6.80 | 2 | https://www.amazon.com/CO-RODE-Tact-Button-Switch-6x6x5mm/dp/B00W0YUV1W/ref=sr_1_2?ie=UTF8&qid=1485275894&sr=8-2&keywords=arduino+push+button
2032 battery | 100 | $14.49 | 1 | https://www.amazon.com/APG-Lithium-Battery-Electronic-Replacement/dp/B0151D7LK2/ref=sr_1_12_s_it?s=hpc&ie=UTF8&qid=1510692868&sr=1-12&keywords=cr2032+battery+pcs
2032 holder | 50 | $12.99 | 2 | https://www.amazon.com/BestTong-Plastic-Vertical-Battery-Sockets/dp/B071KP6X6K/ref=sr_1_14?s=electronics&ie=UTF8&qid=1510692995&sr=1-14&keywords=cr2032+battery+holder+pc
ATTINY85 or 45 | 100 | $96.60 | 1 | https://www.digikey.com/product-detail/en/microchip-technology/ATTINY45-20PU/ATTINY45-20PU-ND/735465
Breadboard | 12 | $9.99 | 9 | https://www.amazon.com/LampVPath-12Packs-solderless-breadboard-Arduino/dp/B01KKE602W/ref=sr_1_12?s=electronics&ie=UTF8&qid=1510690793&sr=1-12&keywords=mini+breadboard+pcs
Notes: Note: ATtiny45 is specified here as it is a little cheaper than the ATtiny85. The 85 has 8k of program memory while 45 has 4k, which is sufficient for this purpose.

## Slide 9: Battery Holder Preparation
Coin cell battery holders do not come with wires that can plug into breadboards. The following mod is required.
This cheap 2032 coin cell battery holder has 3 pins
  Top two are Positive (you only need to use one of them)
  Bottom one is Negative
To use this in our project, we solder one jumper to positive and one to negative. An easy way to do this is as follows:
  Cut one male-male jumper in half
  Strip the ends
  Solder one half to each pin of the battery holder
Wire joints break easily so put a drop of hot glue over each solder joint

## Slide 10: Preparing Battery Holder
Cut jumper in half
Strip the ends
Solder onto battery holder
Add red or black tape to indicate positive voltage
Solder then hot glue
Jumper
Neg.
Pos.
Add Red Flag to indicate Positive
Cut and strip end

## Slide 11: Preparing Battery Holder
Cut jumper in half
Strip the ends
Solder onto battery holder
Add red or black tape to indicate positive voltage
Jumper
Neg.
Pos.
Or Black Flag to indicate Negative
Cut and strip end
Solder then hot glue

## Slide 12: Bag-o-Parts
Mini breadboard
ATtiny microcontroller chip (either ATtiny45 or ATtiny85 work)
2 pushbuttons
3 Resistors: 220, 1,000 (“1K”), 10,000 (“10K”) (1K and 10K only included for experimentation)
Coin cell battery
Coin cell battery holder, with soldered jumper wires and red flag
3 LEDs, different colors. Use 5mm LEDs as they are larger.
Light sensitive resistor
Jumper wires.
  4 cm: 3x
  3 cm: 5x
  2 cm: 2x
  10x total. This is a few more than they need.

## Slide 13: Kit Assembly Line
Bag station
  Start with a bag. Put in a breadboard and ATtiny chip.
  Add 3 resistors to bag: 220 1K 10K
Wire Station (might require several people for wire cutting/striping)
  Add 10 wires
Miscellaneous parts station
  Add 3 LEDs (different colors), 2 pushbuttons, and one photoresistor
  One coin cell battery. Cut package to make easy to open
  Battery holder, make sure it has a red flag on positive (or black flag on negative).

## Slide 14: Background Information
About the ATtiny
The microcontroller used is an ATtiny, which is like the ATmega328 used in Arduino Uno but much smaller. It has only 8 pins compared to 28 pins for the ATmega328 and has less program memory space. With these limitations in mind, it is still a very capable microcontroller that is used in a wide variety of applications. Two of the eight pins are required for ground and power (which can range between 2.7 and 5.5V), and 5 pins provide general purpose digital and analog input/output. (Pin 1 has a special role and is usually not used for GPIO). The ATtiny can be programmed using the standard Arduino software interface. Once the program is uploaded into ATtiny memory it remains there forever and runs whenever power is applied.
Unlike the Arduino Uno, these microcontrollers lack USB connectivity, which makes it somewhat difficult to upload programs into them. One method is to buy a programmer board for about $20, which is offered by many places on the web. A good example is the “Tiny AVR Programmer” available from Sparkfun. This link gives a tutorial: https://learn.sparkfun.com/tutorials/tiny-avr-programmer-hookup-guide
An alternative to buying a commercial board is to convert a standard Arduino Uno into a programmer. This is the approach we take when we need to program a large number of ATtiny chips. Four or five student helpers convert their Arduinos into programmers, and then each student can program 20 or 25 ATtiny chips. This is inexpensive, and also gives our student helpers some good experience with Arduinos. We have a PowerPoint presentation describing how to do this. A good tutorial can be found at http://highlowtech.org/?p=1695
Final notes:
There are three versions of the ATtiny: ATtiny25, ATtiny45, and ATtiny85. These are the same, but with different prices and program memory sizes: 2kB, 4kB, and 8kB.
The program used in this workshop has been tested on ATtiny45 and ATtiny85. It is available by contacting esp4t_tech@uwyo.edu, or the author at kubichek@uwyo.edu.