## Slide 1
Wyoming County Paved Roads Management and Monitoring
Khaled Ksaibati, Ph.D., P.E.
STIC
June, 2014

## Slide 2: Why monitor paved county roads?
Wyoming counties face significant risk if heavy truck traffic increases on many paved county roads.
Notes: In one spring, roads can go from left to right or worse with heavy truck traffic. Any treatment is then expensive.

## Slide 3: What if they fall apart?
No inexpensive options. You can’t blade this.

## Slide 4: Why are we in this situation?
Many roads were paved in the 1950’s, ‘60’s and ‘70’s.
  Designed for lighter loads, if they were designed at all.
  Asphalt was better, aggregate was cheaper.
The asphalt has aged. It is brittle. It cracks easily if heavy loads are applied, specially if the base is soft due to water. Water enters through cracks, softening the base so potholes form and the road falls apart.

## Slide 5: Magnitude of Risk
Chart: 
| Converse | Goshen | Laramie | Platte
Unpaved County Roads Recommended Treatment Costs | 428498 | 1282792 | 957671 | 25559
Total Cattle Guard Replacement Costs | 3229550 | 2015200 | 1698333 | 1813017
Paved County Roads Recommended Improvement Costs | 66289700 | 78669500 | 99594100 | 94936000

## Slide 6: Why do paved roads present a much greater risk than unpaved roads?
Typically 20% or less of a county’s road mileage.
Unpaved roads can be restored with new gravel for about $50,000 per mile.
Paved road restoration costs far more. Even returning to a gravel road could be several hundred thousand dollars per mile.
The annual cost of additional truck traffic on unpaved roads will rarely be over $30,000 per mile, but the one-time cost to restore a destroyed paved road could easily be over $500,000 per mile.

## Slide 7
C
L
12’
12’
Original Pavement Structure
Overlaid Pavement Structure
11½’
11½’
Part of the Problem

## Slide 8: Narrow tops are…
More dangerous.
More prone to edge breakup.

## Slide 9
Objectives
Document current conditions.
  Enable counties to determine impacts of industrial or other activities using paved county roads.
  Compare to state highways
Project future conditions.
Establish maintenance, repair, rehabilitation and reconstruction strategies.

## Slide 10: Pavement Monitoring Benefits
Current conditions identified, allowing appropriate decision to be made.
Impacts from oil and gas drilling and other industries assessed and evaluated.
Other counties’ treatment methods can be quantitatively evaluated and implemented.
WYDOT pavement management system data and decision processes can be applied to county road networks.

## Slide 11: Pavement Monitoring Benefits
Appropriate treatment strategies developed for individual roads at various traffic levels.
Future maintenance and rehabilitation needs projected.
No need for counties with limited resources to develop their own monitoring or analysis methods.
Provide the state legislature with defensible data justifying funding for paved county roads.

## Slide 12: Converse County PSI
PSI > 3.5: Excellent
3.5 > PSI > 3.0: Good
3.0 > PSI > 2.5: Fair
2.5 > PSI: Poor

## Slide 13: Paved County Road Conditions from PSI

## Slide 14: PSI Mileages by Road Class
Chart: County
| POOR | FAIR | GOOD | EXCELLENT | NA
County | 412.02 | 47.33 | 65.8 | 14.14 | 55.5
Chart: State Secondary
| POOR | FAIR | GOOD | EXCELLENT | NA
State Secondary | 667.143 | 515.779 | 545.057 | 670.788
Chart: State Primary
| POOR | FAIR | GOOD | EXCELLENT | NA
State Primary | 465.196 | 821.031 | 829.615 | 1047.873
Chart: Interstate
| POOR | FAIR | GOOD | EXCELLENT | NA
Interstate | 96.95 | 234.747 | 447.466 | 1056.77

## Slide 15: Paved County Road Widths

## Slide 16
Proposed Monitoring Options
Pavement Thicknesses
  Ground Penetrating Radar (GPR)
Pathway Services® van
  Hired annually by WYDOT
  Direct measurements
    Roughness
    Rutting
  Video logs
    May be evaluated in the office to generate a pavement condition index (PCI).
    Provide a log of pavement surface and roadside conditions.

## Slide 17
Video Logs

## Slide 18
Data Compilation and Analytical Options
None
Pavement Condition/Cracking Index (PCI)
Data Summary
Data Analysis

## Slide 19
Pavement Condition Index
From Pathway video logs
  Numerical index from 0 to 100 quantifying the condition of a roadway based on surface distresses.
    Extracted from 1000’ sample sites per mile of paved roadway.
  Manually measured and interpreted through road surface videos collected by Pathway van at highway speeds.

## Slide 20
Ground Penetrating Radar (GPR)
Assessment of asphalt and base thicknesses.
  Essential for design and for durability analyses.
Conducted by a specialized van at highway speeds.

## Slide 21
Options Presented to WACERS

## Slide 22
Inventory and Segmentation
Pathway Services® Van
Roughness
Rutting
Video Logs
GPR Provider (TBD)
Asphalt Surface Thicknesses
Base Thicknesses
Storage on Website
Data Summaries
Tables
Maps
Data Analysis and Reports
Remaining Service Lives
Treatment Recommendations
Comparisons to State Highways
Pavement Condition Index (PCI)

## Slide 23
Option Developed by WACERS

## Slide 24
Inventory and Segmentation
Pathway Services® Van
Roughness
Rutting
Video Logs
GPR Provider (TBD)
Asphalt Surface Thicknesses
Base Thicknesses
Storage on Website
Data Summaries
Tables
Maps
Data Analysis and Reports
Remaining Service Lives
Treatment Recommendations
Comparisons to State Highways
Pavement Condition Index (PCI)

## Slide 25
WACERS’ Recommendation
Collect all data.
  Ground Penetrating Radar (GPR)
  Roughness
  Rutting
  Video logs
    Pavement Condition Index (PCI)
Data Collection Frequency
  Every 2 years
No analysis.
  Many analytical options remain open once the data is collected and stored.

## Slide 26
Data Collection Frequency
First Year: Monitor all paved county roads.
Subsequent Years: Monitor half the state each year.
W – 1,270 miles; E – 1,241 miles
SW – 1,278 miles; NE – 1,233 miles

## Slide 27
Work to be Performed
Wyoming T2/LTAP
  Inventory and Segmentation
  Pavement Condition Index (PCI) processing
  Host website containing raw data
Pathway Services®
  Roughness
  Rutting
  Video Logs
Commercial GPR Tester (TBD)
  Asphalt and Base Thicknesses

## Slide 28
Budget Summary

## Slide 29
Cost Allocation
WYDOT will cover $215,584 in the first year.
$100,000 is requested from the STIC in the first year.
Counties have agreed to cover the running cost for subsequent years.

## Slide 30
Second and Subsequent Years Costs

## Slide 31
Funding
39‑17‑111. Distribution.

## Slide 32
Wyoming County Paved Roads Management and Monitoring
Questions? Comments?
Khaled Ksaibati, Ph.D., P.E.
STIC
June, 2014